## Slide 1: GATX Corporation
ACACSO- Rule 22 TAG Update

## Slide 2: ACACSO UPDATE CHR 22
Overview- CHR 22
ACACSO Nov 2012- CHR 22 Workshop Feedback
EAC & Multi-Level TAG Recap/Update- CHR 22
Questions?

## Slide 3: Overview- CHR 22
Car Hire Rule 22 allows reclaim on assigned cars (specific shipper and national customer pools) while they are empty and idle. There are basically two kinds of Rule 22 reclaims. Reclaim is allowed for cars that are at the loading point and on cars that are held short of the loading point.
Rule 222 Reclaims
“At the Loading Point”
Non-National & National Pool provision, per Car Service Rule 16.
Start/End reclaim time- from date/hour of arrival at the loading point until demurrage free time starts (placement) or until car is released loaded.
Rule 224 Reclaims
“Held Shorts”- Holding point short of the loading point.
Non-National & National Pool provision, per Car Service Rule 16.
Start/end reclaim time- from the time of arrival at the holding point (in excess of 24 hours) until car leaves the holding point.

## Slide 4: ACACSO Nov 2012- CHR 22 Workshop Feedback
At the Nov 2012 ACACSO meeting in San Diego, CA there were 3 workshop sessions that discussed improving CHR 22 for feedback to the EAC’s assigned TAG to review Car Hire Rule 22.
Issues supplied to the EAC’s TAG for CHR 22:
Verbiage in Rule 22 can be confusing and appears complex.
Pool codes not being added in UMLER in a timely manner or incorrect pool headers, which causes counter reclaims. Manual investigation is required to address.
Switch districts used in processing CHR 22 reclaims are inconsistent in size and are not defined for car mark owners, since there is no published source that can be used to confirm that a location is (or is not) within a switch district.
An incorrect type code (222 vs. 224) is sometimes transmitted to the mark owner via CHDX process. An incorrect code can result in counter reclaims and associated manual intervention.

## Slide 5: ACACSO Nov 2012- CHR 22 Workshop Feedback (cont’d)
Suggestions supplied to the EAC’s TAG for CHR 22:
A short line representative and representation from the Reload Steering Committee should be included in an effort to improve CHR 22
Clarify and simplify the language in CHR 22.
Create separate rules for multi-levels cars. Since multi-level equipment are managed differently from other assigned equipment and should be governed by a different set of rules.
Require registration of switch districts in a central repository.
Capping the number of hours subject to reclaim.
Increasing the minimum hours for “held short” reclaims.
Agreement with possibility of centralizing the process (similar to automation of Rule 7 and 8 reclaims). Several issue would need to be address as apart of centralization effort:
  Identification of eligible cars
  Identification and communication of switch districts
  Best handling of stored cars
  Rule simplification and clarification

## Slide 6: EAC & Multi-Level TAG Recap/Update- CHR 22
EAC 2012 Goal Recommendation
    Study of CHR 22- ways to standardize and centralize the process
EAC commission Multi-Level TAG (Sep 2012) to include review goal recommendation of CHR 22.
  First meeting Oct 2012- Industry input requested (ACACSO).
  Second meeting Jan 2013- Industry feedback review only (ACACSO).
  Third meeting April 2013- For CHR 22 there are 5 options being reviewed for recommendation to the EAC.
Five (5) options for review by the TAG regarding CHR 22 in relation to only Multi-Level railcars. (Each assigned to specific TAG members for research and reporting at the TAG’s next meeting)
  Leaving CHR 22 as is
  Eliminating the multi-level fleet from CHR 22 application
  Implementing a 48 hour maximum reclaim
  Allowing reclaim only during specific time frames (i.e. shutdowns)
  Allowing reclaim after a delay of a minimum number of hours

## Slide 7: Questions?
Feedback/Comments/Suggestions