## Slide 1: Rail Vehicle Defect, Condition and Performance Monitoring: 2015 Update
Sr. Principal Investigator
May 14, 2015
RB Wiley

## Slide 2: Automated Vehicle Health Monitoring
Data Integrity
Data flow overview
  Central Detector Data Warehouse Integrated Railway Remote Information Service (InteRRIS® )
  Equipment Health Management System (EHMS)
Alerts (rule supported response required)
Data summaries (informational alerts)
Basic wayside system distinctions

## Slide 3: Implementation of Automated Equipment Health Monitoring & Management
Data Integrity
Carrier
Wayside
System
AEI
Raw Data
Equipment
Identification
Carriers
Outside of Stress-
State Condition
Via Industry
Systems
Car Owners
Industry Systems
InteRRIS®
Stress-
State
Condition
®
Wayside systems feed InteRRISÒ after identifying the car with automatic equipment identification (AEI)
InteRRISÒ identifies a “stress-state” condition
InteRRISÒ communicates with Railinc systems for processing

## Slide 4: EHMS Vehicle Health Detectors on North American Freight Railroads
Data Integrity
Current
  Wheel Impact Load Detector System (167 reporting/181 in database)
  Truck Steering Performance (14/22)
  Acoustic Bearing (33/39)
  High Speed Stability* (Truck Hunting: 89/95)
  Optical Geometry Detectors (28/30)
  Wheel Profile (11/28)
Pending
  Brake Performance
2009: 128
Detectors installed and maintained by railroads
Must be coupled with AEI — direct or virtual
*Added feature to some wheel impact load detectors

## Slide 5: Industry Alerts
Data Integrity
Wheel Impact Load Detector (WILD)
  Window Open: ≥ 65 kips
  Opportunistic Repair: ≥ 80 kips
  Condemnable: ≥ 90 kips
  Final Alert: ≥ 140 kips
Truck Hunting Detector (THD)
  Window Open: ≥ 0.2 once
  Condemnable: ≥ 0.5 once or ≥ 0.35 twice in 12 months
Acoustic Bearing Detector (ABD), Condemnable only
  TADS®: Growler 5
Truck Performance Detector (TPD), Condemnable only
  TPDL: LAHRLV ⃰ ≥ 1.05 twice in 12 months
  TPDG: Gage Spread ≥ 28+ kips (by degree curve) twice in 12 months
⃰ Lead Axle High Rail Lateral/Vertical

## Slide 6: Automated Equipment Health Management
Data Integrity
Does it work?
Chart: Wheel Impact Statistics WILD Hits/1000 Wheels*
Chart: Wheel Impact Statistics 140 kip+ WILD Hits/1000 Wheels*

## Slide 7: Equipment Health Monitoring Systems for AAR Interchange Fleet (> 1.4-million rail vehicles)
Data Integrity
InteRRIS®: Central Detector Data Warehouse History
  Receive, analyze, and transmit rail vehicle performance data
    Total fleet size of intensively managed: approaching 1,250,000 rail vehicles (85% of NA fleet)
    300+ detectors worldwide \ 500-million records per month
  Detailed performance data tracking
  Alert determination for Advanced Technology Safety Initiative — now Equipment Health Monitoring Committee
EHMS: Central Vehicle Health Alerts Status
  Rule-based alerts
  Informational (Data Summary) alerts
  Operational October 1, 2004
  Alerts closed by repair or auto-closed

## Slide 8
Data Integrity
8
1
0
0
0
0
1
0
0
0
2
0
0
0
M
i
l
e
s
N
W
a
y
s
i
d
e
D
e
t
e
c
t
o
r
D
i
s
t
r
i
b
u
t
i
o
n
.
B
a
s
e
d
o
n
U
S
G
S
D
L
G
.
1
:
2
5
,
5
0
0
,
0
0
0
,
G
e
o
g
r
a
p
h
i
c
P
r
o
j
e
c
t
i
o
n
,
D
D
.
2015
(
c
)
,
T
r
a
n
s
p
o
r
t
a
t
i
o
n
T
e
c
h
n
o
l
o
g
y
C
e
n
t
e
r
,
I
n
c
.
14
25
180
20
28
14
03/14/2015

## Slide 9: Newly Available (at the industry level) Condition and Performance Monitors
Data Integrity
Optical Geometry Detector (OGD)
  In production InteRRIS® (since Monday, March 16)
Wheel Profile Detector (WPD) and Wheel Profile Measurement System (WPMS)
  InteRRIS® release: ~ end of May

## Slide 10
Data Integrity
TPD: force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS®-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM®-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.

## Slide 11: Truck Performance (Curving) Detector
00860cun -
1
Ideal Site for
Bi-directional
Traffic
Curvatures
4° – 6°
Curvatures
4° – 6°
Measurements:
Vertical Load
Lateral Load
AOA

## Slide 12
TPD: force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS®-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.
Data Integrity

## Slide 13: Wheel Impact Load Detectors
TTCI Testing of Impact Load Detectors
Electronic Equipment
Notes: Basic overview of WILD
  Note older, massive size vs current small footprint
  Tangent (illustration is older 10 crib layout)
  16+ cribs (sensor pairs) - sometimes includes lateral force sensors

## Slide 14: Truck Hunting Detector
Instrumented cribs measure vertical & lateral wheel loads
HI values typically:
  HI > 0.5: Severe Hunting
  0.20 < HI > 0.5: Moderate Hunting
  HI < 0.20: Limited or no Hunting
To establish a hunting index (HI) over a length of track

## Slide 15
Data Integrity
TPD: force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS®-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.

## Slide 16: Trackside Acoustic Detection System

## Slide 17
Data Integrity
TPD: force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS®-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.

## Slide 18: Rail Bearing Acoustic Monitor

## Slide 19
Data Integrity
TPD: force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS®-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.

## Slide 20
TBOGI-OGD (Optical Geometry Detector)
Optical Geometry Detector
Single-Unit
3-Units are THD capable

## Slide 21
Data Integrity
TPD (Truck Performance Detector): force-based truck curving performance monitor located in a reverse curve.
WILD: force-based out-of-round wheel detector; located on tangent track. Some (89) WILDs include THD or lateral instability monitoring capability.
TADS-ABD (Trackside Acoustic Detector System – Acoustic Bearing Detector): Identifies defective bearings by sound signature; located on tangent track.
RailBAM-ABD: Identifies defective bearings by sound signature; located on tangent track.
TBOGI-OGD (Optical Geometry Detector): Laser-based truck geometry and performance detector located on tangent track. Seven of the OGD sites have THD capability (TBOGI-HD).
WPMS: Laser- or vision-based wheel profile measuring system; located on tangent track.

## Slide 22
Wheel Profiles: Laser-based
Wheel Profile Measurement System or Wheel Profile Detector
Notes: Images or profile plots supplement the measurement data

## Slide 23: Wheel Profile Measurement System or Wheel Profile Detector
Wheel Profiles: Vision-based
Notes: Images or profile plots supplement the measurement data

## Slide 24: Detector and Monitor Overview: AEI
AEI
OGD

## Slide 25: Vehicle Health Monitoring Systems
Data Integrity
Databases (InteRRIS® & EHMS)
Data Summary
Wayside Machine Vision Technology
Wayside Performance Monitoring
Wayside Condition Detection
Cracked Axle Detector Cracked Wheel Detector
Thermal Scan
Acoustic Bearing Detector
Low Air Hose Detector
Dragging Equipment Detector
Truck Hunting Detector
Truck Performance Detector
Wheel Impact Load Detector
Warm Bearing Trending
Wheel Temperature Trending
Wheel Profile Module
Brake Shoe Module
Optical Geometry
Automated Safety Appliance Inspection System
Automated Structural Inspection System
Fully Automated Train Scan

## Slide 26: Questions?
Data Integrity