## Slide 1: ACACSO Car Service Rules 7 to 12
November 11, 2014

## Slide 2: CSR 7 Interchange - Error Movements
Responsibility for Cars Delivered
Prompt Interchange of Cars
Delayed Interchange
Lack of Necessary Documents
Error Delivery – Receiving Carrier Options
Error Delivery – Notifications and Definitions

## Slide 3: Responsibility for Cars Delivered
A car is considered “delivered” to a connecting railroad when it is placed on the agreed upon interchange track
All cars delivered in interchange should be preceded by an Advanced Interchange Consist (EDI 418)
  Roads can be penalized for failure to provide necessary forwarding instructions once EDI procedures are in place between two roads
The receiving road is responsible for the cars, contents, and car hire after receipt of the proper data for forwarding.

## Slide 4: Prompt Interchange of Cars
Interchange should occur within 24 hours after arrival or release at the interchange
Exceptions include:
  Traffic covered by embargo or equipment alert
  Cars covered by notification from delivering road and confirmation from receiving road that it is unable to take the cars
  Cars which can not physically be placed on the designated interchange track

## Slide 5: Delayed Interchange
Delivering road may seek protection from car hire under Car Hire Rule 15
Procedures include:
  Holding road notifies AAR who notifies receiving road
  Receiving road agrees or fails to respond then TOL occurs (6 hrs for class 1 and 12 for others)
  Receiving road does not agree, AAR notifies delivering road and no TOL occurs
  Delivering road must then interchange within 24 hours
Notes: 12 hours for non-class 1 railroads

## Slide 6: Lack of Necessary Documents
If a loaded car is offered without forwarding data, receiving road should request (EDI 425) it from delivering road
Return the car to delivering road or proper road within the same switch district
If empty, move to or in the direction of the home road per Car Service Rule 2, Special Car Orders or Directives
Delivering road is responsible for any intermediate switching and car hire charges

## Slide 7: Error Delivery – Notifications and Definitions
Delivered to a road not in the waybill route
The empty or load indicator is wrong
Waybill is missing, incomplete, or inaccurate
Empty delivered in violation of Car Service Rule 2, Special Car Orders or Directives
Empty delivered to a road in switching service but not ordered by the switching road

## Slide 8: CSR 8 Advertisements
Advertisements or banners upon any freight, passenger car, or locomotive is prohibited except:
  For photographic purposes while the car is rested
  On passenger cars for special train movements
Why ?
Promotes asset utilization for moving freight cars into and out of shipper or commodity assignment.

## Slide 9: CSR 9 Steamship, Ferry or Barge Restrictions
Railroad cars must not be loaded for or delivered to steamship, ferry or barge line for transportation by water, except:
  In interstate commerce by common carriers by water between points within the continental US
  With owner permission under SCO30
Why ?
Tighter management of freight cars by keeping them in the North American Rail Network.

## Slide 10: CSR 10 - Responsibility for Charges When Necessary to Transfer or Rearrange Lading
The delivering road is responsible when:
  Defective equipment that is not safe
    AAR Interchange Rule 92
  Car is not loaded in compliance with AAR Circulars
    https://www.aarpublications.com
  Violations of US DOT rules governing transportation of explosives and other dangerous articles.
Notes: Rule 92 examples include: hazardous leaking, defective, clearances

## Slide 11: CSR 10 - Continued
The switch or origin road is responsible when:
  Load exceeds stenciled load limit
  Overloads in violation of AAR Circulars (unless overload results in shifted laden en route)
  Loaded car is prohibited in interchange
        AAR Interchange Rule 90
Notes: Rule 90 is overage age (40 year cars)

## Slide 12: CSR 10 - Continued
The originating road is responsible when:
  Gross weight of loaded car exceeds published weight restrictions
  Dimensions of loaded cars being in excess of published clearances of any road in the routing
        Railway Line Clearances
  Cars loading in violation of Car Service Rule 9
Notes: Rule 90 is overage age (40 year cars)

## Slide 13: CSR 10 - Continued
The receiving road is responsible when:
  Cars were properly loaded at origin
  Cars can not be handled to destination as a result of a disability of the receiving line
  Receiving road desires to transfer to save the cost of car hire
Notes: Rule 90 is overage age (40 year cars)

## Slide 14: CSR 11 Weighing of Cars
First road haul carrier shall provide scale weights
  Scale weights may be waived if any of the following endorsements are on the waybill:
  Shippers Weight Agreement
  Destination Weight Agreement
  Tariff Authority Weight
  Manifest Weight -TOFC and FAK
  Official Weight (US only - FGIS)
  Grain Exchange Weight (US only - Grain Exchange)
Notes: FGIS – Federal Grain Inspection Service
Grain Exchange – Weights authorized and controlled by a grain exchange
TOFC –
FAK – Freight All Kinds

## Slide 15: CSR 11 - Continued
  A penalty of $75 per car included for failure to comply
  The point at which loading is completed is considered the origin of a stop-off car and determines the road responsible.
  Shortlines that do not have scales should make arrangements for weighing with their connecting roads.
        Reference Appendix B to the Code of Car Hire Rules
Notes: Subsequent road charges originating road or road in the waybill route that does not forward weights to them.
Billed within 3 months after the month in which penalty charge accrued. Paid within 3 months after the month in which penalty charge received.
Appendix B: Reference Car Service Rule 11(G), Car Hire Rules Introduction
Rules Governing Settlement of the Use of Foreign Railroad-Owned Freight Cars by Short
Line Railroads, Which are Less Than 100 Miles in Length.
1. The Code of Car Hire Rules shall apply, except as herein after modified or amended.
2. Short line connections:
a. Short lines having but one connecting railroad may settle with that road for the use of foreign freight
equipment, if no alternative methods of settlement are available.
b. Short lines having connection(s) with more than one railroad will settle with the car owner for the use of
foreign freight equipment except when authorized to settle with connecting railroads by those railroads.
3. Settlements under Rule 2 shall be made promptly after the close of each calendar month and shall include all car
hire accruing during that month.
4. The connecting carrier with which settlements are made under Rule 2 shall report all car hire accruing on such
cars to the car owner, in accordance with the Code of Car Hire Rules.
5. Junction reports prescribed by Car Hire Rule 10 need not be made for cars subject to Rule 2.

## Slide 16: CSR 12 Cars Containing Refuse
Cars offered in interchange as empties that are found to contain refuse can be rejected by the receiving road
Empty boxcars and gondolas with grades X, Y or Z are excluded
  X Grade A that contains refuse
  Y Grade B that contains refuse
  Z Grade C that contains refuse
        Reference Car Service Rule 14
Notes: RULE 14 – Contaminating Commodities
A. Box cars grade A or B per AAR Car Grade System, or refrigerator cars, must not be loaded with K graded
commodities listed in Appendix A, list of K grade commodities.
B. Municipal Waste (STC Code 4029114; Car Grade W) may only be loaded in equipment assigned for that purpose.
C. If a Box car is loaded in violation of A or B above and it becomes necessary to renew floors, lining or sheathing
(including associated parts), or portions thereof, in order to restore car to previous loading classification because of
contamination due to such loading, the cost of the repairs, notwithstanding any other provision of these rules, shall be
assumed by the road (either switching or road haul) responsible for furnishing the car for such loading.