## Slide 1: Rule 22 Automation ACACSO – MAY 2014

## Slide 2: Background
Recommended by Centralized Car Hire TAG (CCH) in September 2013
Unanimously approved by Equipment Assets Committee (EAC) in January 2014
TAG appointed by EAC and meetings began in February 2014

## Slide 3: Tag Members
GATX
Greenbrier Companies
GE
Progress Rail Services
Railinc
ShipXpress
TTX Company
CN
CP
CSXT
GWRR
KCS
NS
UP

## Slide 4: TAG Goals
Create a set of standard business rules
Simplify the existing Rule 22 verbiage
Low cost industry implementation – LCS message
Not to change the intent and current application of the rule
Notes: .

## Slide 5: Serving Areas vs. Switch Districts
Serving areas - defined by each carrier based on:
  Geography – 1st two digits of SPLC
  Railroad operations
Information availability
  Automated notification when changes are made
Dispute
  Arbitration through Car Hire Rule 17

## Slide 6: Shipper Pools –Eligible Equipment
Assigned to a specific shipper pool.
  Umler will reflect a pool number with a carrier’s numeric code as the first three digits (not 999 or 998) and the Pool Type in Umler must be “C” or
  The Transportation/Transportation Condition Code will be C, DC or EC

## Slide 7: Shipper Pools – Eligible Carriers
Car Assigned to a specific shipper pool
  Only the pool operator or carriers designated by bilateral agreement are eligible for relief.
  For example, cars in pool 5551234 (NS) will be allowed holding point and loading point relief. If NS establishes a bilateral agreement to allow road XYZ to load the cars. Road XYZ will only be allowed loading point relief.

## Slide 8: Joint Pools – Eligible Equipment
Assigned to a joint pool
  Umler will reflect a pool assignment that starts with 998 and the Pool Type in Umler must be “C” or
  The Transportation/Transportation Condition Code will be C, DC or EC and
  The handling carrier will be a participant in the pool.

## Slide 9: Joint Pools – Eligible Carriers
Cars Assigned to a joint pool
  Only the carriers that participate in the pool will be eligible for relief.
  For example, if pool 9981234 is operated by carrier A and B, either carrier A or B will be allowed relief.
  TAG members are continuing to review joint pool operations and the possible impact/likelihood of bilateral agreements.
Notes: .

## Slide 10: National Pools – Eligible Equipment
Assigned to a national shipper pool
  Umler will reflect a pool assignment that starts with 999 and the Pool Type in Umler must be “C” or
  The Transportation/Transportation Condition Code will be DN or N
  The North American Boxcar Pool (NABP) and specific equipment pools operated by TTX will be excluded from the relief process.

## Slide 11: National Pools – Eligible Carriers
Cars assigned to a national shipper pool
  Any carrier that has contributed equipment to the pool will be eligible for relief.
  TAG members are continuing to review relief implications for short lines that load and hold national pool cars.

## Slide 12: Bilateral Agreements
Bilateral agreements
  Carriers must be able to negotiate bilateral agreements that allow cars assigned on one carrier to be used on another.
  The system will provide a user interface for the pool operator to enter the pool number and the carrier entitled to relief on the cars.
User interface

## Slide 13: Loading Point – Subject to Demurrage
System design:
  All equipment subject to demurrage/storage unless updated by carrier
  Beginning transaction – empty arrival
  Ending transaction – empty placement (actual/constructive)
  Missing events:
    Arrival – no relief allowed
    Placement – relief ends on first loaded record
LCS Transactions:
Arrival at Loading Point E Delivery - R222
Placement E Receipt - R222
Release Loaded L

## Slide 14: Loading Point – Exempt from Demurrage
System design:
  All equipment subject to demurrage/storage unless updated by carrier
  Beginning transaction – empty arrival
  Ending transaction – release load or first loaded event
  Missing events:
    Arrival – no relief allowed
    Release – relief ends on first loaded record
LCS Transactions:
Arrival at Loading Point E Delivery R222
Placement E
Release Loaded L Receipt R222

## Slide 15: Holding Point
System design:
  Beginning transaction – empty arrival
  Ending transaction –empty departure (same location)
    < 24hrs between beginning and ending transactions
  Missing events:
    Arrival – no relief allowed
    Release – no relief allowed
LCS Transactions:
Arrival at Holding Point E Delivery - R224
Departure from Holding Point E Receipt - R224

## Slide 16: Scenarios Out of Scope
New system will not consider:
  Cars ordered home
  Cars ordered to a new loading point
Relief handled through Car Hire Rule 13 and 22

## Slide 17: Management Tools
Informational reports
  Multilevel equipment with missing pool assignment
  Multilevel equipment in non participating pool assignment
Financial Reports
  Summary and detail reports of the dollars associated with the various reclaim types.

## Slide 18: Next Steps
TAG actions
  Complete proposed business rules
  Complete proposed Rule 22 verbiage change
Potential 2015 project
  Requires approval from EAC and RPSWC

## Slide 19: Questions
Robert Sanford
Director Revenue Accounting Support Services
Robert.Sanford@nscorp.com
404-529-1011